segment * 16 + offset

The memory segmentation model, where the real (physical) address is calculated as segment * 16 + offset, was used in the original Intel x86 architecture for several key reasons:
### 1. Compatibility with 16-bit Architecture
The x86 architecture started as a 16-bit architecture (like the Intel 8086 and 8088 processors). These processors had a 20-bit address bus, which allowed them to address up to 1 MB (2^20 bytes) of memory. However, the general-purpose registers in these processors were only 16 bits wide, limiting the range of a single memory address to 64 KB (2^16 bytes).
By using segmentation, a 16-bit segment register and a 16-bit offset could be combined to form a 20-bit physical address:
- Segment: A 16-bit value representing the base address of a memory segment.
- Offset: A 16-bit value representing an offset within the segment.
The formula segment * 16 + offset (where segment * 16 effectively shifts the segment value left by 4 bits) allows for the 16-bit values to be used to calculate a 20-bit physical address. This method provided access to a much larger memory space (1 MB) than what would have been possible with just 16-bit addresses.

### Origin of the Term "x86"
1. Intel 8086 Processor: The x86 architecture traces its roots back to the Intel 8086 microprocessor, introduced in 1978. The "86" in x86 originally comes from the last two digits of the 8086 model number.
2. Subsequent Processors: After the success of the 8086, Intel continued to develop processors in the same architectural family, each building upon the capabilities of its predecessors. The processors that followed included the 80186, 80286, 80386, and 80486. The naming convention remained consistent with the "86" suffix, which led to the shorthand x86 to represent this family of processors.

x86 architecture register

The x86 architecture, which is used in many CPUs, has several registers that are used for different purposes. Here’s a summary of the key registers in the x86 CPU:
### General Purpose Registers
1. EAX (Accumulator Register): Used for arithmetic operations and holds the result of operations.
2. EBX (Base Register): Typically used to hold the base address for memory operations.
3. ECX (Counter Register): Primarily used for loop counters and string operations.
4. EDX (Data Register): Used for I/O operations and also as an extension of the accumulator for some arithmetic operations (e.g., multiplication and division).
### Index and Pointer Registers
1. ESI (Source Index): Used as a source pointer for string operations.
2. EDI (Destination Index): Used as a destination pointer for string operations.
3. EBP (Base Pointer): Points to the base of the stack frame, typically used to reference function parameters and local variables.
4. ESP (Stack Pointer): Points to the top of the current stack frame, used for stack operations.
### Segment Registers
1. CS (Code Segment): Points to the segment containing the current program code.
2. DS (Data Segment): Points to the segment containing the program's data.
3. SS (Stack Segment): Points to the segment containing the stack.
4. ES (Extra Segment): Additional segment register for data.
5. FS and GS: Extra segment registers available for general-purpose use.
### Instruction Pointer and Flags
1. EIP (Instruction Pointer): Points to the current instruction being executed.
2. EFLAGS (Flags Register): Contains flags that control the CPU's operation and reflects the status of the processor. Flags include:
- CF (Carry Flag): Indicates carry or borrow out of the most significant bit.
- ZF (Zero Flag): Indicates that the result of an operation was zero.
- SF (Sign Flag): Indicates the sign of the result of an operation.
- OF (Overflow Flag): Indicates arithmetic overflow.
- PF (Parity Flag): Indicates if the number of set bits is odd or even.
- AF (Adjust Flag): Used in binary-coded decimal (BCD) arithmetic.
- DF (Direction Flag): Controls string operations direction.
- IF (Interrupt Enable Flag): Controls the handling of interrupts.

Segment:[base+index*scale+displacement]

The notation segment:[base + index * scale + displacement] is used in the x86 assembly language to describe addressing modes for accessing memory locations. This notation is particularly useful in understanding how to reference complex memory addresses efficiently. Let's break down each component in detail:
### Components of the Addressing Mode
1. Segment:
  1. The segment part specifies a memory segment. In x86, memory is divided into segments, each identified by a segment register (like CS, DS, ES, FS, GS, SS).
  2. Segments help in organizing memory and provide a method to reference a block of memory. When a segment is specified in the notation, it means that the address is relative to the base of that segment. If no segment is explicitly stated, the default segment register is typically used based on the context (e.g., DS for data, SS for stack).
2. Base Register:
  1. The base register is one of the general-purpose registers (EAX, EBX, ECX, EDX, EBP, ESI, EDI, etc.). It holds the base address of the memory location.
  2. This register contains an initial value or a base pointer to which other values can be added to compute a final memory address.
3. Index Register:
  1. The index register is another general-purpose register. It is typically used to hold an offset or index value.
  2. This is useful for accessing elements in an array or structure, where the index register points to the current element or offset from the base.
4. Scale Factor:
  1. The scale factor is a multiplier that can be applied to the index register. In x86, the scale factor can be 1, 2, 4, or 8.
  2. This is used to multiply the index value by the size of each element in an array. For example, if accessing an array of 4-byte integers, the scale factor would be 4.
5. Displacement:
  1. Displacement is a constant value or an immediate offset added to the address calculation.
  2. This can be used to access a specific field within a structure or to adjust the final address by a certain amount.
### Address Calculation
The formula segment:[base + index * scale + displacement] is used to compute the effective address (EA) in memory. Here’s how it works:
1. Indexing into Arrays:
  1. When accessing elements of an array, the base register might point to the start of the array, the index register could contain the index of the element, and the scale would be the size of each element.
  2. Example: Suppose base = EBX points to the start of an array of integers, index = ECX is the index of the desired element, and scale = 4 (size of an integer). The effective address of the desired element would be EBX + ECX * 4.
2. Accessing Structure Fields:
  1. When accessing fields within a structure, the base register might point to the base of the structure, while the displacement would be the offset of the field from the start of the structure.
  2. Example: If base = EAX points to the start of a structure and displacement = 8 is the offset of a specific field within the structure, the effective address for that field would be EAX + 8.
3. Combined Addressing:
  1. You can combine all these components to form more complex addresses. For example, in a two-dimensional array, base might point to the start of the array, index might represent the column index, and displacement might be used to reach a specific element after calculating the correct row offset.
  2. Example: segment:[EBX + ECX * 4 + 12] would mean: start at the memory location pointed to by EBX, add four times the value in ECX (perhaps indexing into an array of integers), and then add 12 bytes (perhaps offsetting into a specific field or adjusting the index).

Makefile

A Makefile is a build automation tool primarily used in software development to compile and link programs or perform other repetitive tasks. It defines rules, dependencies, and commands to automate processes like building, cleaning, or packaging software.

### 1. Basic Structure
A Makefile consists of:
- Targets: What you want to build (e.g., an executable, object file, or script).
- Dependencies: Files that a target depends on (e.g., source files or other targets).
- Commands: Shell commands to build the target.

Example:
target: dependencies
    command

How kernel get loaded?
Loading into Memory
The bootloader (bootloader.bin) is responsible for loading kernel.bin into memory during the boot process. Typically, here's how this happens:
#### a. Bootloader Reads File System
The bootloader, once executed by the BIOS, reads the FAT12 file system to locate kernel.bin using directory entries and the file allocation table.
#### b. Kernel Load Address
- The bootloader decides where in memory to load the kernel.
- A common convention in x86 systems is:
  - Low Memory (0x7E00, 0x10000, or higher): For protected-mode kernels.
  - High Memory: For advanced operating systems.
#### c. Reading Kernel into Memory
Using BIOS interrupt 0x13 (disk services), the bootloader reads the kernel.bin file sector-by-sector and copies it to the designated memory address.
#### d. Jumping to Kernel
Once the kernel is loaded into memory, the bootloader jumps to the kernel's entry point, starting its execution.

### What Does bootloader.bin Do with FAT12?
The bootloader uses FAT12 to locate and load the kernel or additional components needed for the operating system. Here’s how it interacts with FAT12:
#### a. BIOS Loads the Bootloader
The BIOS loads the first sector (512 bytes) of the floppy disk, where bootloader.bin resides, into memory at 0x7C00 and transfers control to it.
#### b. Bootloader Reads FAT12 Structures
- The bootloader reads the FAT12 data structures (e.g., root directory and file allocation table) to locate files like kernel.bin.
  - Root Directory: Finds the kernel.bin file and determines its starting cluster.
  - File Allocation Table: Tracks which clusters the file occupies.
#### c. Bootloader Loads the Kernel
Once the bootloader locates the file, it uses BIOS disk interrupts (e.g., int 0x13) to read the corresponding sectors from the disk and load the file into memory.
#### d. Transfers Control to Kernel
After loading the kernel into memory, the bootloader jumps to the kernel's entry point to begin executing it.