segment * 16 + offset

The memory segmentation model, where the real (physical) address is calculated as segment * 16 + offset, was used in the original Intel x86 architecture for several key reasons:
### 1. Compatibility with 16-bit Architecture
The x86 architecture started as a 16-bit architecture (like the Intel 8086 and 8088 processors). These processors had a 20-bit address bus, which allowed them to address up to 1 MB (2^20 bytes) of memory. However, the general-purpose registers in these processors were only 16 bits wide, limiting the range of a single memory address to 64 KB (2^16 bytes).
By using segmentation, a 16-bit segment register and a 16-bit offset could be combined to form a 20-bit physical address:
- Segment: A 16-bit value representing the base address of a memory segment.
- Offset: A 16-bit value representing an offset within the segment.
The formula segment * 16 + offset (where segment * 16 effectively shifts the segment value left by 4 bits) allows for the 16-bit values to be used to calculate a 20-bit physical address. This method provided access to a much larger memory space (1 MB) than what would have been possible with just 16-bit addresses.

### Origin of the Term "x86"
1. Intel 8086 Processor: The x86 architecture traces its roots back to the Intel 8086 microprocessor, introduced in 1978. The "86" in x86 originally comes from the last two digits of the 8086 model number.
2. Subsequent Processors: After the success of the 8086, Intel continued to develop processors in the same architectural family, each building upon the capabilities of its predecessors. The processors that followed included the 80186, 80286, 80386, and 80486. The naming convention remained consistent with the "86" suffix, which led to the shorthand x86 to represent this family of processors.