segment * 16 + offset

The memory segmentation model, where the real (physical) address is calculated as segment * 16 + offset, was used in the original Intel x86 architecture for several key reasons:
### 1. Compatibility with 16-bit Architecture
The x86 architecture started as a 16-bit architecture (like the Intel 8086 and 8088 processors). These processors had a 20-bit address bus, which allowed them to address up to 1 MB (2^20 bytes) of memory. However, the general-purpose registers in these processors were only 16 bits wide, limiting the range of a single memory address to 64 KB (2^16 bytes).
By using segmentation, a 16-bit segment register and a 16-bit offset could be combined to form a 20-bit physical address:
- Segment: A 16-bit value representing the base address of a memory segment.
- Offset: A 16-bit value representing an offset within the segment.
The formula segment * 16 + offset (where segment * 16 effectively shifts the segment value left by 4 bits) allows for the 16-bit values to be used to calculate a 20-bit physical address. This method provided access to a much larger memory space (1 MB) than what would have been possible with just 16-bit addresses.

### Origin of the Term "x86"
1. Intel 8086 Processor: The x86 architecture traces its roots back to the Intel 8086 microprocessor, introduced in 1978. The "86" in x86 originally comes from the last two digits of the 8086 model number.
2. Subsequent Processors: After the success of the 8086, Intel continued to develop processors in the same architectural family, each building upon the capabilities of its predecessors. The processors that followed included the 80186, 80286, 80386, and 80486. The naming convention remained consistent with the "86" suffix, which led to the shorthand x86 to represent this family of processors.

x86 architecture register

The x86 architecture, which is used in many CPUs, has several registers that are used for different purposes. Here’s a summary of the key registers in the x86 CPU:
### General Purpose Registers
1. EAX (Accumulator Register): Used for arithmetic operations and holds the result of operations.
2. EBX (Base Register): Typically used to hold the base address for memory operations.
3. ECX (Counter Register): Primarily used for loop counters and string operations.
4. EDX (Data Register): Used for I/O operations and also as an extension of the accumulator for some arithmetic operations (e.g., multiplication and division).
### Index and Pointer Registers
1. ESI (Source Index): Used as a source pointer for string operations.
2. EDI (Destination Index): Used as a destination pointer for string operations.
3. EBP (Base Pointer): Points to the base of the stack frame, typically used to reference function parameters and local variables.
4. ESP (Stack Pointer): Points to the top of the current stack frame, used for stack operations.
### Segment Registers
1. CS (Code Segment): Points to the segment containing the current program code.
2. DS (Data Segment): Points to the segment containing the program's data.
3. SS (Stack Segment): Points to the segment containing the stack.
4. ES (Extra Segment): Additional segment register for data.
5. FS and GS: Extra segment registers available for general-purpose use.
### Instruction Pointer and Flags
1. EIP (Instruction Pointer): Points to the current instruction being executed.
2. EFLAGS (Flags Register): Contains flags that control the CPU's operation and reflects the status of the processor. Flags include:
- CF (Carry Flag): Indicates carry or borrow out of the most significant bit.
- ZF (Zero Flag): Indicates that the result of an operation was zero.
- SF (Sign Flag): Indicates the sign of the result of an operation.
- OF (Overflow Flag): Indicates arithmetic overflow.
- PF (Parity Flag): Indicates if the number of set bits is odd or even.
- AF (Adjust Flag): Used in binary-coded decimal (BCD) arithmetic.
- DF (Direction Flag): Controls string operations direction.
- IF (Interrupt Enable Flag): Controls the handling of interrupts.

Segment:[base+index*scale+displacement]

The notation segment:[base + index * scale + displacement] is used in the x86 assembly language to describe addressing modes for accessing memory locations. This notation is particularly useful in understanding how to reference complex memory addresses efficiently. Let's break down each component in detail:
### Components of the Addressing Mode
1. Segment:
  1. The segment part specifies a memory segment. In x86, memory is divided into segments, each identified by a segment register (like CS, DS, ES, FS, GS, SS).
  2. Segments help in organizing memory and provide a method to reference a block of memory. When a segment is specified in the notation, it means that the address is relative to the base of that segment. If no segment is explicitly stated, the default segment register is typically used based on the context (e.g., DS for data, SS for stack).
2. Base Register:
  1. The base register is one of the general-purpose registers (EAX, EBX, ECX, EDX, EBP, ESI, EDI, etc.). It holds the base address of the memory location.
  2. This register contains an initial value or a base pointer to which other values can be added to compute a final memory address.
3. Index Register:
  1. The index register is another general-purpose register. It is typically used to hold an offset or index value.
  2. This is useful for accessing elements in an array or structure, where the index register points to the current element or offset from the base.
4. Scale Factor:
  1. The scale factor is a multiplier that can be applied to the index register. In x86, the scale factor can be 1, 2, 4, or 8.
  2. This is used to multiply the index value by the size of each element in an array. For example, if accessing an array of 4-byte integers, the scale factor would be 4.
5. Displacement:
  1. Displacement is a constant value or an immediate offset added to the address calculation.
  2. This can be used to access a specific field within a structure or to adjust the final address by a certain amount.
### Address Calculation
The formula segment:[base + index * scale + displacement] is used to compute the effective address (EA) in memory. Here’s how it works:
1. Indexing into Arrays:
  1. When accessing elements of an array, the base register might point to the start of the array, the index register could contain the index of the element, and the scale would be the size of each element.
  2. Example: Suppose base = EBX points to the start of an array of integers, index = ECX is the index of the desired element, and scale = 4 (size of an integer). The effective address of the desired element would be EBX + ECX * 4.
2. Accessing Structure Fields:
  1. When accessing fields within a structure, the base register might point to the base of the structure, while the displacement would be the offset of the field from the start of the structure.
  2. Example: If base = EAX points to the start of a structure and displacement = 8 is the offset of a specific field within the structure, the effective address for that field would be EAX + 8.
3. Combined Addressing:
  1. You can combine all these components to form more complex addresses. For example, in a two-dimensional array, base might point to the start of the array, index might represent the column index, and displacement might be used to reach a specific element after calculating the correct row offset.
  2. Example: segment:[EBX + ECX * 4 + 12] would mean: start at the memory location pointed to by EBX, add four times the value in ECX (perhaps indexing into an array of integers), and then add 12 bytes (perhaps offsetting into a specific field or adjusting the index).

Makefile

A Makefile is a build automation tool primarily used in software development to compile and link programs or perform other repetitive tasks. It defines rules, dependencies, and commands to automate processes like building, cleaning, or packaging software.

### 1. Basic Structure
A Makefile consists of:
- Targets: What you want to build (e.g., an executable, object file, or script).
- Dependencies: Files that a target depends on (e.g., source files or other targets).
- Commands: Shell commands to build the target.

Example:
target: dependencies
    command

How kernel get loaded?
Loading into Memory
The bootloader (bootloader.bin) is responsible for loading kernel.bin into memory during the boot process. Typically, here's how this happens:
#### a. Bootloader Reads File System
The bootloader, once executed by the BIOS, reads the FAT12 file system to locate kernel.bin using directory entries and the file allocation table.
#### b. Kernel Load Address
- The bootloader decides where in memory to load the kernel.
- A common convention in x86 systems is:
  - Low Memory (0x7E00, 0x10000, or higher): For protected-mode kernels.
  - High Memory: For advanced operating systems.
#### c. Reading Kernel into Memory
Using BIOS interrupt 0x13 (disk services), the bootloader reads the kernel.bin file sector-by-sector and copies it to the designated memory address.
#### d. Jumping to Kernel
Once the kernel is loaded into memory, the bootloader jumps to the kernel's entry point, starting its execution.

### What Does bootloader.bin Do with FAT12?
The bootloader uses FAT12 to locate and load the kernel or additional components needed for the operating system. Here’s how it interacts with FAT12:
#### a. BIOS Loads the Bootloader
The BIOS loads the first sector (512 bytes) of the floppy disk, where bootloader.bin resides, into memory at 0x7C00 and transfers control to it.
#### b. Bootloader Reads FAT12 Structures
- The bootloader reads the FAT12 data structures (e.g., root directory and file allocation table) to locate files like kernel.bin.
  - Root Directory: Finds the kernel.bin file and determines its starting cluster.
  - File Allocation Table: Tracks which clusters the file occupies.
#### c. Bootloader Loads the Kernel
Once the bootloader locates the file, it uses BIOS disk interrupts (e.g., int 0x13) to read the corresponding sectors from the disk and load the file into memory.
#### d. Transfers Control to Kernel
After loading the kernel into memory, the bootloader jumps to the kernel's entry point to begin executing it.

### Why is FAT12 Used in This Bootloader?
The bootloader in your code uses FAT12 because it needs to load the kernel (or other files) from the disk. FAT12 helps achieve this because:
1. Simple File Organization:
  1. FAT12 organizes the floppy disk into clusters and tracks which clusters belong to which files.
  2. Without a filesystem, the bootloader would have no way to locate the kernel file (kernel.bin) on the disk.
2. Compatibility:
  1. FAT12 is widely supported by BIOS routines (int 13h) and operating systems like MS-DOS.
  2. The bootloader uses BIOS disk services to read data from the disk, which expect the disk to follow a known format like FAT12.
3. Flexibility:
  1. With FAT12, you can add or modify files on the disk (e.g., kernel.bin) without rewriting the entire bootloader.
  2. If there were no filesystem, any file changes would require recalculating exact byte offsets for the new file.

### Why Use FAT12 in the Bootloader Specifically?
The bootloader needs to:
1. Find the kernel file on the disk.
2. Load the kernel into memory.
With FAT12:
- The kernel file is stored as a named file (kernel.bin) in the FAT12 filesystem.
- The bootloader:
  - Reads the FAT12 metadata (like the root directory and FAT table) to locate kernel.bin.
  - Uses the metadata to load the file into memory.

File System

A filesystem is a way to organize and store data on a storage device like a floppy disk, hard drive, or USB drive. It defines how files are named, stored, retrieved, and managed. A filesystem ensures that data is structured and accessible. Without it, data on storage devices would just be a raw stream of bytes, making it difficult to locate specific files or manage space efficiently.

### Common Filesystems
1. FAT12, FAT16, FAT32 (File Allocation Table):
  1. Used in floppy disks, early USB drives, and embedded systems.
  2. Simple and widely supported.
2. NTFS (New Technology File System):
  1. Windows’ primary filesystem.
  2. Supports large files, encryption, and advanced permissions.
3. EXT2/EXT3/EXT4:
  1. Popular in Linux.
  2. Advanced journaling and large file support.
4. HFS+/APFS:
  1. Used by macOS for advanced storage features.

### Detailed Layout
Section	Purpose	Size
Boot Sector	Metadata about the filesystem and boot instructions.	1 sector (512 bytes on a floppy)
FAT Table(s)	Tracks cluster allocation for the entire disk.	Varies (typically 9*2 sectors each)
Root Directory	Stores file metadata (e.g., names, attributes, starting clusters).	Fixed size (e.g., 224 entries)
Data Area	Contains the actual file and directory contents in clusters.	Remaining disk space

Boot sector calculation ,means how much space does boot sector required.

Next is File allocation table which will be calculated from below method. There are 2 FAT copy of each other just for data recovery purpose.

Number of sector = 2*9 = 18 sector

Next is Root directory .
Each entry is 32 byte therefore calculation is done as :

(224*32+512-1 / 512) = 14 sector

Fat uses block called cluster , like disk use sector.

Root Directory:

### Explanation of First Cluster Low and High
1. First Cluster Low (2 bytes):
  1. Represents the lower 16 bits of the starting cluster number.
  2. Since FAT12 is designed for small disks (and 12-bit clusters), this field is typically enough to hold the cluster number on its own.
2. First Cluster High (2 bytes):
  1. Represents the higher 16 bits of the starting cluster number.
  2. This field is used in FAT32, where cluster numbers can exceed 16 bits. In FAT12, this field is unused or set to 0.

Why Subtract 2 from the Cluster Number?
- Clusters start at 2 in the FAT file system (cluster 0 and 1 are reserved for special purposes).
- Therefore, when converting a cluster number to an offset in the Data Region, you subtract 2 to align it with the Data Region start.

---------------------------------------------------------------------------------

Is fat is the part of kernel.bin or bootloader.bin?

The FAT (File Allocation Table) is not part of either kernel.bin or bootloader.bin directly. Instead, it is a data structure stored on the disk that both the bootloader and the kernel may use to locate files, such as kernel.bin. Here's how it fits into the broader context:

### 1. FAT in Bootloader Context
The bootloader is responsible for loading the kernel or other files from the disk into memory. To do this, it must:
- Understand the disk's file system, such as FAT12.
- Locate and read the FAT to find the clusters where the file resides.
The bootloader typically:
1. Reads the boot sector to load the FAT12 metadata.
2. Uses the FAT to locate the clusters containing kernel.bin.
3. Loads the kernel into memory cluster by cluster, following the FAT's links.

### 2. FAT in Kernel Context
Once the kernel is loaded and running, it may need to access files on the disk. For this:
The kernel also interacts with the FAT (or other file systems) to read or write files.
In this case, the FAT is used by the kernel's file system driver to manage files stored on the disk.

### Is FAT Part of Bootloader or Kernel?
1. Bootloader:
  1. The bootloader reads the FAT to find and load files (like the kernel).
  2. However, the FAT is stored on the disk, not compiled into the bootloader binary.
2. Kernel:
  1. The kernel may also interact with the FAT to manage files during its operation.
  2. Like the bootloader, it reads the FAT from the disk as needed.

### Why Isn't FAT Embedded in Bootloader or Kernel?
1. Separation of Concerns:
  1. The FAT is a dynamic structure that changes when files are added or removed from the disk.
  2. Embedding the FAT in the bootloader or kernel would make it static and unusable for managing a live file system.
2. Disk Independence:
  1. Keeping the FAT on the disk allows any operating system or bootloader supporting FAT to access files.